3D Numerical Simulation on the Rockslide Generated Tsunamis

Tso-Ren Wu1, Mei-Hui Chuang1, Chung-Yue Wang2, and Chia-Ren Chu2

1Graduate Institute of Hydrological and Oceanic Sciences,

National Central University, Jhongli City, Taoyuan County, Taiwan

2Department of Civil Engineering, National Central University

Jhongli City, Taoyuan County, Taiwan

The rockslide generated tsunami is one of the most devastating nature hazards. However, the involvement of the moving obstacle and dynamic free-surface movement makes the numerical simulation a difficult task. To describe both the fluid motion and solid movement at the same time, we newly developed a two-way fully-coupled moving solid algorithm with 3D LES turbulent model. The free-surface movement is tracked by volume of fluid (VOF) method. The two-step projection method is adopted to solve the Navier-Stokes type government equations.

In the new moving solid algorithm, a fictitious body force is implicitly prescribed in MAC correction step to make the cell-center velocity satisfied with the obstacle velocity. We called this method the implicit velocity method (IVM). Because no extra terms are added to the pressure Poission correction, the pressure field of the fluid part is stable, which is the key of the two-way fluid-solid coupling. Because no real solid material is presented in the IVM, the time marching step is not restricted to the smallest effective grid size. Also, because the fictitious force is implicitly added to the correction step, the resulting velocity is accurate and fully coupled with the resulting pressure field.

We validated the IVM by simulating a floating box moving up and down on the free-surface. We presented the time-history obstacle trajectory and compared it with the experimental data. Very accurate result can be seen in terms of the oscillating amplitude and the period. We also presented the free-surface comparison with the high-speed snapshots.

At the end, the IVM was used to study the rock-slide generated tsunamis (Liu et al., 2005). Good validations on the slide trajectory and the free-surface movement will be presented in the full paper. From the simulation results (Fig. 1), we observed that the rockslide generated waves are manly caused by the rebounding waves from two sides of the sliding rock after the water is dragging down by the solid downward motion. We also found that the turbulence has minor effect to the main flow field. The rock size, rock density, and the steepness of the slope were analyzed to understand their effects to the maximum runup height.

The detailed algorithm of IVM, the validation, the simulation and analysis of rockslide tsunami will be presented in the full paper.

Figure 1. Snapshots of the free-surface elevation with streamlines for the rockslide tsunami simulation.